SMesh Mega2
V2

---
Objectives
- Describe the electronics and construction where they different with build standard 1
- Mega is
  - LiIon battery
  - PM sensor, BME but no INA
  - Solar charging option
  - RPi Z Logger with shutdown switch included
- It is useful for
  - Prototype for drone sensor
  - Diagnostics in the field and lab
  - Short duration deployments
INA was needed to monitor
12V battery power. Meshtastic
has built-in monitor for LiIon.

---
Battery Capacity and Voltage
- LiIon batteries are about 10 Ah and 3.7 to 4.2 V
- Battery life in hours is Capacity in Ah divided by average current drawn from battery in amperes.
- The Meshtastic radio/computer/display and the BME are 3.7V
- The PM sensor and RPi, and battery charging from Meshtastic, require 5V
- The battery supplies 3.7V and a 3.7 → 5V DC-DC converter is used to provide 5V.
  - Switching power supply has 90%+ efficiency
  - Input current does not equal output current
  - More about switchers <here>

---
Solar Charger
- Mega’s battery is somewhat undersized:
  - 10 Ah * 3 LiIon batteries = 30 Ah
  - Average current draw is 0.5 A with the logger on
  - It can run for almost 3 days
- Solar panels can extend battery life
- Connect via a schottky diode to the 5V Meshtastic input and there is a battery charger on the Meshtastic which prevents overcharging.
- More about solar chargers <here>

---
Mega: PM sensor works only when powered by USB

---
Add RPi, 5V power for PM sensor
Can’t charge battery
Possibly too much current in the DC-DC converter

---
Charges battery when USB connected and SW1 on
PM sensor gets 5V
Adequate current handling in DC-DC converters

---
Schottky Diodes
- We use them for lower forward voltage drop, which has lower power loss.
- The two diodes we use form a “wired or” circuit. Power for the 5V DC-DC converters comes from either the battery or the USB .. without connecting them together.
- More information about “Schottkys” is <here>

---
Dipole Antenna
- Best to always connect an antenna when powering up a Meshtastic, as no antenna has been known to occasionally destroy the transmitter.
- The simplest form of an antenna is a dipole. One side becomes positive in voltage, one side becomes negative as the electromagnetic wave passes through on receive, or is generated on transmit
Wire becomes +
Wire becomes -
Cable to radio

---
Ground Plane antenna
Also possible to reflect one side over a ground plane, which acts like a mirror.
In the plane above the ground, it
behaves like a dipole
In the plane below the ground, no
antenna is visible.
---Ground Plane --
Cable to radio

---
Approximation of ground plane
- Just a wire coming from the radio serves as the monopole, while the radio and battery themselves form the ground plane, albeit imperfect
- Instead of straight wires, the antenna can be made physically shorter by coiling the wire.

---
Mega2
Shutdown
switch
Battery
switch
Antenna

---
The shutdown switch
- The RPi, and most cached file systems, require notification before shutdown
  - Directories and files are cached in RAM for speed
  - At shutdown, the OS writes them to disk
Capacitor reduces
sensitivity to
local electrical noise
sudo nano /boot/firmware/config.txt
dtoverlay=gpio-shutdown,gpio_pin=3
More info about the shutdown switch